## Slide 1: Overflow
When adding 2 n-bit numbers it is possible to get a n+1 bit result if there is a carry out.
The rule – if the carry-in to the sign bit position differs from the carry-out position of the sign bit, then an overflow has occurred.
Example 1: Add (+70) to (+80) is:
  Carries 0 1 overflow
  +70 0 100 0110
  +80 0 101 0000
  +150 1 001 0110

## Slide 2
Example 2: Add (-70) and (-80)
Carries 1 0 overflow
  -70 1 011 1010
  -80 1 011 0000
  -150 0 110 1010
  The circuit
  If, V=1 overflow
  else no overflow
Carry into sign bit
Carry out from sign bit
Overflow