## Slide 1: Addition/Subtraction of Signed Binary Numbers

## Slide 2
Binary Number Representation
Unsigned Representation
Signed Representation
Signed-Magnitude Form
1’s Complement Form
2’ Complement Form
Only for
positive Numbers
For both Positive & Negative Numbers

## Slide 3: Sign-Magnitude Representation
In the sign-magnitude representation, a number is represented in its binary form as:
The most significant bit (MSB) represents the sign.
1 in the MSB bit position denotes a negative number; and 0 denotes a positive number.
The remaining (n −1) bits represent the magnitude of the number.
This representation is used both for positive and negative binary numbers.
The following examples illustrate the sign-magnitude representation:

## Slide 4: 1's Complement Representation
1’s complement is another way of feeding the negative binary number to the computer.
In 1’s complement method , negative numbers are represented by taking 1’s complement of positive representation of a number.
Example : -33 =?
33 is represented as (100001)2
In 8 bit notation, +33 is represented as (0 0100001)2
-33 = 1’s complement of (+33)
= 1’s complement of (0 0100001)2
= 1 1011110
Now, (-33) is represented in 1’s complement form as (1 1011110)2
Sign bit
Magnitude

## Slide 5: 2's Complement Representation
In 2’s complement method , negative numbers are represented by taking 2’s complement of positive representation of a number.
Example : -33 =?
33 is represented as (100001)2
In 8 bit notation, +33 is represented as (0 0100001)2
-33 = 2’s complement of (+33)
= 2’s complement of (0 0100001)2
= 1’s complement of (0 0100001)2 + 1
= 1 1011110 + 1
= 1 1011111
Now, (-33) is represented in 2’s complement form as (1 1011111)2
Magnitude
Sign bit

## Slide 6: Addition by Signed 2’s Complement Form
  The addition of two signed binary numbers represented in Signed 2's- complement form is obtained by adding the two numbers including their sign bits.
  A carry out of the sign-bit position is discarded.
  Example 1: (+6) + (+13) = ?
  (+6) 00000110
  + (+13) + 00001101
  +19 00010011
  Example 2: (-6) + (+13) = ?
  (-6) 11111010 (2’s complement of +6)
  + (+13) + 00001101
  +7 00000111

## Slide 7
  Example 3: (+6) + (-13) = ?
  (+6) 00000110
  + (-13) + 11110011 (2’s complement of +13)
  -7 11111001
  Example 4: (-6) + (-13) = ?
  (-6) 11111010 (2’s complement of +6)
  + (-13) + 11110011 (2’s complement of +13)
  -19 11101101
As result is –ve
So, for final answer, take 2’s complement of (11111001) accept the sign bit =10000111= (-7)10
As result is –ve
So, for final answer, take 2’s complement of (11101101) accept the sign bit =10010011= (-19)10